## Slide 1: UV-C Disinfection Box project
N. Beni, S. Buontempo, I. Crotty, E. Dimovasili, N.Dupont, A. Lanaro, D. Lomidze, S. Lusin, R. Perruzza, G. Pugliese, Z. Szillasi
UV-C Photon Destroys Virus and Bacteria
Green fluorescence: test samples incubated with N1H1 virus
Blue fluorescence: number of sterilized cells
Source: Sci Rep 8, 2752 (2018). https://doi.org/10.1038/s41598-018-21058-w
98.2% of viruses destroyed by 15 J/m2 dose at 75% RH using 4.9 eV photons -> 254nm UVC
Source: https://www.ncbi.nlm.nih.gov/pmc/articles/PMC3298127/

## Slide 2: CFL Based UVC Disinfection Box
Box design:
  Aluminium box
  UVC source: 6 x Mercury vapour based CFL
  54 W total power (electrical)
  Mirrored Inner Surface / Uniform Illumination
Features:
  Console for local or remote (wifi) control
  Time based dose regulation
  Dose, temperature and humidity monitoring
  Interlock system for radiation and high voltage safety
A first prototype of UV-C disinfection box was designed and built by our CMS colleague David Lomidze in Germany.
Glowing UVC radiation from 1st prototype
Philips 9W CFL

## Slide 3
  Status and plan
  CSC lab in 904 building has been prepared
  Material procurement on going
  Box assembling starting this week
  The CMS team is working to produce and test several disinfection boxes to disinfect tools, materials, PPE.
CFL Based UVC Disinfection Box @ CERN
Circuit diagram

## Slide 4: CFL Based UVC Disinfection Box @ CERN
UV-C sensors: GUVC-T21GH
Distributor: https://www.tecnosens.it/
Box validation @ CERN
Dose measurements
UV-C sensors will be installed in order to measure:
Irradiation uniformity and optimization of the lamp location
Dose measurements vs. time
Based on our estimation: ~500 uWSec/cm2 x 20 sec irradiation
 10 mJ/cm2 dose (in the fairest point 16cm away)
 5 min irradiation delivers 150 mJ/cm2 dose
Electrical and radiation safety
Preliminary irradiation validation:
Tools of different materials (plastic, metal, etc) will be irradiated. The integrity will checked with visual inspection
Masks will be irradiated and efficiecy valuated
  Final validation will be performed in Biological laboratories specialized on studies of SARS-CoV-2 virus