## Slide 1: Leak Test cooling system with reference Volume
Tests & Data by Iuri Bagaturia

## Slide 2: Acceptance Limit Graphical Definition
CMS Limit
5E-04 [mbar.l/s]
Pressure
Time [secs]
1E-05 [mbar.l/s]
1E-06
[mbar.l/s]
ACCEPTABLE REGION
NOT ACCEPTED REGION
Leak rate calculated from Roberto’s gas leak formula

## Slide 3: Past events
Single point Temp correction introduced, not perfect as not homogeneous.
The ref. vol. has been introduced as we had difficulties getting good values
A leak was found on the jig at a late date
Tests with soft copper had led to poor results.
Bad assembly technique has led to poor results.

## Slide 4: Results. 1 2tests were done with ref vol and SM14
 |  |  | Slope , bar/sec |  | L-Rate , mbar∙l/sec |  |  |  | 
N | File name | calculated time interval, hr | Reffernce tube | SM14 | Reffernce tube | SM14 | Ref Tube Positive values | SM14 ABS values | SM - Ref vol Leak Rate
1 | CoolSM14NewRefHardCu09Aug001 | 3.32 | 1.316E-06 | -1.585E-05 | 3.10E-04 | -3.74E-03 | 3.10E-04 | 3.740E-03 | 3.429E-03
2 | CoolSM14NewRefHardCu13Aug002 | 7.64 | 3.611E-07 | -9.970E-06 | 8.52E-05 | -2.35E-03 | 8.52E-05 | 2.353E-03 | 2.268E-03
3 | CoolSM14NewRefHardCu14Aug004 | 20.47 | -5.388E-07 | -1.279E-05 | -1.27E-04 | -3.02E-03 | 1.27E-04 | 3.017E-03 | 2.890E-03
4 | CoolSM14NewRefHardCu15Aug005 | 2.56 | -7.625E-06 | -6.389E-06 | -1.80E-03 | -1.51E-03 | 1.80E-03 | 1.508E-03 | -2.917E-04
5 | CoolSM14NewRefHardCu15Aug006 | 0.66 | -5.293E-07 | -1.440E-05 | -1.25E-04 | -3.40E-03 | 1.25E-04 | 3.399E-03 | 3.274E-03
6 | CoolSM14NewRefHardCu15Aug008 | 17.92 | 3.290E-07 | -1.710E-05 | 7.76E-05 | -4.04E-03 | 7.76E-05 | 4.037E-03 | 3.959E-03
7 | CoolSM14NewRefHardCu16Aug01 | 0.44 | -2.037E-06 | -6.528E-06 | -4.81E-04 | -1.54E-03 | 4.81E-04 | 1.541E-03 | 1.060E-03
8 | CoolSM14NewRefHardCu16Aug02 | 38.17 | 3.115E-08 | -1.267E-05 | 7.35E-06 | -2.99E-03 | 7.35E-06 | 2.991E-03 | 2.983E-03
9 | CoolSM14NewRefHardCu18Aug01 | 15.42 | -3.648E-07 | -1.388E-05 | -8.61E-05 | -3.27E-03 | 8.61E-05 | 3.275E-03 | 3.189E-03
10 | CoolSM14NewRefHardCu19Aug01 | 4.83 | 3.880E-07 | -1.497E-05 | 9.16E-05 | -3.53E-03 | 9.16E-05 | 3.533E-03 | 3.442E-03
11 | CoolSM14NewRefHardCu20Aug01 | 9.25 | -5.062E-07 | -1.439E-05 | -1.19E-04 | -3.40E-03 | 1.19E-04 | 3.397E-03 | 3.277E-03
12 | CoolSM14NewRefHardCu20Aug07 | 0.05 | -7.306E-05 | -1.033E-04 | -1.72E-02 | -2.44E-02 | 1.72E-02 |  | 

## Slide 5: Leak test results for the Ref Vol
Chart: 
Leak Rates Ref | 0.00031047 | 8.5221e-05 | 0.00012716 | 0.0017994 | 0.00012491 | 7.7632e-05 | 0.00048082 | 7.3508e-06 | 8.6085e-05 | 9.1559e-05 | 0.00011946
Short test | 0.017242
CMS ref Leak rate | 0.0005

## Slide 6: Duration dependance
Chart: Abs Leak rate vs Duration
| 3.3166666666666669 | 7.6388888888888893 | 20.469444444444445 | 2.5555555555555554 | 0.66111111111111109 | 17.916666666666668 | 0.43611111111111112 | 38.166666666666664 | 15.416666666666666 | 4.833333333333333 | 9.25 | 5.1944444444444446E-2
Abs Leak rate vs Duration | 0.00031047 | 8.5221e-05 | 0.00012716 | 0.0017994 | 0.00012491 | 7.7632e-05 | 0.00048082 | 7.3508e-06 | 8.6085e-05 | 9.1559e-05 | 0.00011946 | 0.017242
It would appear that the duration necessary for the calculation of leak rate is 5 hours, to be verified with raw data

## Slide 7: A leaky SM14 giving rather similar results, less dispersion.
The literature states that the dP/dt method is unsuitable for this level of leak rate. The above result and other experience illustrates this.
Chart: 
Abs leak Rates SM14 | 0.0037399 | 0.002353 | 0.0030173 | 0.0015077 | 0.0033988 | 0.0040367 | 0.0015407 | 0.0029907 | 0.0032749 | 0.0035334 | 0.0033969

## Slide 8: Previous results
[mbar.l/s]
CMS Limit 5.00E-04
SM002 1.2500E-04
SM003 3.3170E-04
SM004 8.6232E-04
SM005 6.2000E-05
SM006 2.8150E-04
SM007 2.9400E-04
SM008 1.9618E-03
Chart: 
| SM002 | SM003 | SM004 | SM005 | SM006 | SM007 | SM008
SM2-8 | 0.000125 | 0.0003317 | 0.00086232 | 6.2e-05 | 0.0002815 | 0.000294 | 0.0019618
CMS Limit | 0.0005
One bad case SM 008
One poor value SM004

## Slide 9: Conclusion
Test may take up to one day. 30 mins preparation.
As the ref vol is approx 10% of values obtained for SMs that are not within the CMS spec then a re-test should be done.
Approx ½ of the 18 have been tested with only one poor value.
Require 10 days to measure the remaining SMs.
Correct assembly technique is vital over tightening is detrimental.