## Slide 1: Tables & degrees of freedom in GIF++
Ian Crotty
10 March 2015

## Slide 2: An object has 6 degrees of freedom

## Slide 3: We want 4 degrees
“X” transvers
Horizontal
“Y” Vertical
X Rotation
“Z” Longitudinal Horizontal
Beam Line

## Slide 4: The x and z are for free but not precise
Wheels on the base.
How to obtain the reproducible points
What level of precision

## Slide 5: We have this frame with “Y” translation
Alu frame dimensions 110cm x 215cm

## Slide 6: Motorised “Y” axis
Motor driven mechanism for translation in “Y” approx. 60cm
Manual Rotation about “Y”

## Slide 7: Details of frame
Sliders for vertical translation require cleaning

## Slide 8: Vertical position definition
The present system can be monitored with a shielded camera

## Slide 9: Conclusion
We have a frame that must be modified to accommodate the ration in “X” horizontal axis
and mount the chamber(s).
The height must be adjusted to the beam height.
The frame requires some renovation, cleam and grease.
Require cable and power supply for E. Motor
Require camera to give the vertical position for remote operation